## Slide 1
Jacob Kamminga
Dataset: Horse Movement Data and Analysis of its Potential for Activity Recognition
Jacob Kamminga, Nirvana Meratnia, Paul Havinga

## Slide 2: Animal Activity Recognition (AAR)
AAR provides large amount of information regarding the animal and its environment
  Livestock management
  E-health for pets
  Detection of environmental effects such as forest fires and poaching
  Movement ecology
  Wildlife conservation
Notes: Large amount of info not only about the animal, but also its environment

## Slide 3: Data Acquisition
14 horses and 4 ponies
7 days of data collection

## Slide 4: Sensors
GCDC Human Activity Monitor (HAM)
3D Accelerometer, 100Hz
3D Gyroscope, 100Hz
3D Magnetometer, 12Hz

## Slide 5: Sensor Placement
Notes: Around Neck so that not halter or saddle is needed. Sensor location also used to monitor wildlife such as zebra.

## Slide 6
Notes: Outdoor pasture

## Slide 7
Notes: Mostly grazing outside

## Slide 8
Notes: Paddock

## Slide 10: Labeling

## Slide 11: Column description
Column name | Description
Ax | Raw data from accelerometer x-axis
Ay | Raw data from accelerometer y-axis
Az | Raw data from accelerometer z-axis
Gx | Raw data from gyroscope x-axis
Gy | Raw data from gyroscope y-axis
Gz | Raw data from gyroscope z-axis
Mx | Raw data from magnetometer x-axis
My | Raw data from magnetometer y-axis
Mz | Raw data from magnetometer z-axis
A3D | l2-norm (3D vector) of accelerometer axes
G3D | l2-norm (3D vector) of gyroscope axes
M3D | l2-norm (3D vector) of magnetometer axes
label | Label that belongs to datapoint
segment | Segment identifier
subject | Subject identifier
Notes: Date Time?!

## Slide 13: Number of 2-second samples
Chart: 
| Labeled | Unlabeled
 | 93303 | 1191658
Labeled | 93303
Unlabeled | 1191658
Notes: with 50% overlap

## Slide 14: Number of samples per activity
Notes: 17 activities

## Slide 15
Notes: A column-normalized column summary displays the number of correctly and incorrectly classified observations for each predicted class as percentages of the number of observations of the corresponding predicted class.

## Slide 16: Dataset use cases
Unsupervised representation learning
Sensor-Orientation-Independent AAR
Gait analysis and comparison
Transfer learning
AAR for similar animals such as donkeys or zebras

## Slide 17: Conclusions
Large dataset, especially unlabeled data
  Particularly suitable for unsupervised representation learning
More labeled data for subset of subjects and activities
Lesson learned: think about prospective dataset uses outside own research objective prior to collection
Notes: Little additional effort might extend dataset usage range

## Slide 18: Thanks for your attention
Jacob Kamminga
University of Twente

## Slide 19: Number of 2-second samples per activity
Activity | null | standing | walking-rider | walking-natural | trotting | galloping | eating | other | total
nr samples | 1191658 | 5297 | 35425 | 3609 | 25782 | 4036 | 18110 | 1044 | 1284961
fraction of labeled |  | 6% | 38% | 4% | 28% | 4% | 19% | 1% | 
Notes: with 50% overlap

## Slide 21: Evaluation
Naïve Bayes classifier
Accelerometer data from 6 subjects and 6 activities
Leave-one-subject-out cross validation
Transform 3 axes into 3D vector (l2-norm)
Features: 21 summary statistics (mean, std, … )

## Slide 22
Activity | null | unknown | walking_rider | trotting_rider | grazing | standing | galloping_rider | walking_natural | head_shake | scratch_biting | galloping_natural | trotting_natural | eating | jumping | shaking | rolling | fighting | rubbing | scared | total
Galoway | 62155 | 23264 | 9653 | 6374 | 4315 | 1750 | 1030 | 1402 | 59 | 170 | 13 | 49 | 16 |  | 4 | 13 | 25 |  |  | 110292
Bacardi | 92775 | 9850 | 1317 | 1981 | 1116 | 245 | 288 | 360 |  | 22 | 40 |  |  |  | 13 |  |  | 6 |  | 108013
Driekus | 85468 | 11271 | 4024 | 2670 | 2465 | 341 | 310 | 270 | 55 | 14 | 13 | 3 | 31 |  | 4 | 23 |  |  |  | 106962
Patron | 78536 | 15156 | 5150 | 3385 | 1951 | 1244 | 709 | 388 | 37 |  | 5 | 17 |  |  |  | 31 |  |  |  | 106609
Happy | 68468 | 13606 | 8896 | 7032 | 5062 | 1186 | 689 | 746 | 238 | 8 | 7 | 6 | 1 |  |  |  |  |  |  | 105945
Zonnerante | 90431 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 90431
Duke | 81885 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 81885
Viva | 69441 | 4413 | 1066 | 700 |  | 58 | 82 | 79 | 5 | 4 |  |  |  |  |  |  |  |  | 1 | 75849
Flower | 75741 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 75741
Pan | 68628 | 1575 | 241 |  |  | 36 |  | 44 |  |  |  |  |  |  |  |  |  |  |  | 70524
Porthos | 67080 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 67080
Barino | 66517 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 66517
Zafir | 38424 | 10349 | 5078 | 3546 | 1091 | 347 | 826 | 161 | 105 | 23 | 9 | 13 |  | 12 |  |  |  |  |  | 59984
Niro | 43563 | 2740 |  |  | 85 | 20 |  | 2 |  |  |  |  |  |  |  |  |  |  |  | 46410
Sense | 38823 | 1569 |  |  | 1977 | 39 |  | 157 | 120 | 44 | 15 | 6 |  |  |  |  | 6 |  | 2 | 42758
Blondy | 31579 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 31579
Noortje | 17777 | 2878 |  |  |  | 31 |  |  |  |  |  |  |  |  |  |  |  |  |  | 20686
Clever | 17696 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 17696
total | 1094987 | 96671 | 35425 | 25688 | 18062 | 5297 | 3934 | 3609 | 619 | 285 | 102 | 94 | 48 | 12 | 21 | 67 | 31 | 6 | 3 | 1284961

## Slide 23: Evaluation
Naïve Bayes classifier
Leave-one-subject-out cross validation
Accelerometer data from 6 subjects and 6 activities
Transform 3 axes into 3D vector (l2-norm)
Features: 21 summary statistics (mean, std, … )
Balancing
  Majority class: random under-sampling
  Minority class: oversampling using SMOTE

## Slide 28: Summary statistics
Domain | Feature | Description
Time | Maximum | Maximum value
 | Minimum | Minimum value
 | Mean | Average value
 | Standard deviation | Measure of dispersion
 | Median | Median value
 | \nth{25} percentile | The value below which \SI{25}{\%} of the observations are found
 | \nth{75} percentile | The value below which \SI{75}{\%} of the observations are found
 | Mean low pass filtered signal | Mean value of DC components
 | Mean rectified high pass filtered signal | Mean value of rectified AC components
 | Skewness of the signal | The degree of asymmetry of the signal distribution
 | Kurtosis | The degree of 'peakedness' of the signal distribution
 | Zero crossing rate | Number of zero crossings per second
Frequency | Principal frequency | Frequency component that has the greatest magnitude
 | Spectral energy | The sum of the squared discrete FFT component magnitudes
 | Frequency entropy | Measure of the distribution of frequency components
 | Frequency magnitudes | Magnitude of first six components of FFT analysis

## Slide 29: Why Animal Activity Recognition?

## Slide 30
Detection of Environmental Events
Notes: Human activities, Effects of climate change and environmental pollution
on animals

## Slide 31
Poaching detection
Notes: Human activities, Effects of climate change and environmental pollution
on animals

## Slide 32
Livestock Management
Notes: Activity recognition of livestock not only enables better healthcare but also improve management (e.g. show when cow can be inseminated)

## Slide 33
Wildlife Conservation and Movement Ecology
Notes: Previous work subsequent retrieval and shows heterogeneity